Sampling schemes for instruments in

Massachusetts Bay Internal Wave Experiment

| Site | Mooring type | Instrument type | Sampling interval | Variables and sampling scheme |
| --- | --- | --- | --- | --- |
| A | Surface | Seacat | 60 s | T, C, one sample every 60 s |
| B | Surface | tpod | 120 sec | T, one sample every 120 s |
| B | Subsurface | tpod | 120 s | T, one sample every 120 s |
|  |  | VMCM | 60 s | V, vector-average every 60 s; T, one sample at end of interval |
|  |  | FSI | 90 s | V, vector-average every 90 s; T, one sample at end of interval |
|  |  | Tide | 60 s |  |
| B | Horizontal | FSI | 90 s | V, average every 90 s; T, one sample at end of interval |
|  |  | SBE | 15 s | T, one sample every 15 s |
|  |  | Microcat | 15 s | T, C, one sample every 15 s |
|  |  | tpod | 120 s | T, one sample every 240 s |
| B | Tripod | ADCP | 60 s | V, average of 60 one-second pings every 60 s in 2 m bins |
|  |  | MIDAS | 60 s | V and P, 60 s averages at .5 Hz; T, C and Tr, single sample every 60 s in center of interval |
| C | Surface | Microcat | 15 s | T, C, one sample every 15 s |
| C | Subsurface | Microcat | 15 s | T, C, one sample of every 15 s |
|  |  | SeaCat | 50 s | T, C, and Tr, one sample of every 50 s |
| C | Tripod | ADCP | 60 s | V, average of 60 one-second pings every 60 s in 2 m bins. |
|  |  | Camera | 1 hour | Single picture |

Variables Key:  C = Conductivity; P = Pressure; T = Temperature; Tr = Light transmission; V = Current velocity.

Instrument Key:  ADCP = Acoustic Doppler current Profiler; Camera = Benthos 35 mm camera; FSI = Falmouth Scientific, Inc.; MIDAS = USGS Multiparameter Intelligent Data Logging System; SBE = Sea Bird Electronics; tpod = ; VMCM = Vector Measuring Current Meter