| MOORING NUMBER | AREA OF STUDY | SITE | LATITUDE | LONGITUDE | WATER DEPTH (from mooring log) | DEPLOYMENT NUMBER | DATE DEPLOYED | DATE RECOVERED | INSTRUMENT PROVIDER | INSTRUMENT SERIAL NUMBER | INSTRUMENT DEPTH | Frequency | Sampling Interval | Sampling Scheme | Platform | DATAFILES | NOTES |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Temperature + Salinity | Water Flow | Waves | Sediment | Pressure | Sonar |  |
| 720 | Myrtle Beach | 1 | 33° 38.979′ N | 78° 47.361′ W | 11.3 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | ADCP #159 | 126 cmab |  | 900 s | 5 min every 15 min | micropod | ---------------- | ---------------- | 7201adc-a.nc | 7201adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 722 | Myrtle Beach | 2 | 33° 38.923′ N | 78° 50.942′ W | 9.4 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | ADCP #767 | 123 cmab |  | 900 s | 5 min every 15 min | micropod | ---------------- | ---------------- | 7221adc-a.nc | 7221adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 722 | Myrtle Beach | 2 | 33° 38.923′ N | 78° 50.942′ W | 9.4 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | CT #1045 | 96 cmab |  | 300 s |  | micropod | 7222sc-b.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 722 | Myrtle Beach | 2 | 33° 38.923′ N | 78° 50.942′ W | 9.4 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | PT #127 | 47 cmab |  | 300 s |  | micropod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7223pt-a.nc | ---------------- | ---------------- |  |
| 723 | Myrtle Beach | 2 | 33° 38.959′ N | 78° 50.959′ W | 9.3 m | 1 | 10/4/2003 | 1/21/2004 | USGS-WH | CT #707 | 1 mbs |  | 300 s |  | USGS surface buoy | 7231mc-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | MC #307 for 2nd half |
| 724 | Myrtle Beach | 3 | 33° 46.433′ N | 78° 40.924′ W | 9.4 m | 1 | 10/28/2003 | 1/22/2004 | USC | ADCP #2014 | 126 cmab |  | 900 s | 5 min every 15 min | micropod | ---------------- | ---------------- | 7241adc-a.nc | No Waves | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 724 | Myrtle Beach | 3 | 33° 46.433′ N | 78° 40.924′ W | 9.4 m | 1 | 10/28/2003 | 1/22/2004 | USGS-WH | CT #392 | 98 cmab |  | 300 s |  | micropod | 7242sc-b.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 724 | Myrtle Beach | 3 | 33° 46.433′ N | 78° 40.924′ W | 9.4 m | 1 | 10/28/2003 | 1/22/2004 | USGS-WH | PT #128 | 46 cmab |  | 300 s |  | micropod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7243pt-a.nc | ---------------- | ---------------- |  |
| 725 | Myrtle Beach | 3 | 33° 46.470′ N | 78° 40.906′ W | 10.8 m | 1 | 10/4/2003 | 1/21/2004 | USGS-WH | CT #726 | 1 mbs |  | 300 s |  | USGS surface buoy | 7251mc-b.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | CT #263 for 2nd half |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USC | ADV #A300 | 39.3 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 7261advs-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | Data only until ~23 Nov. '03 due to biofouling |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USC | ADV #A302 | 50.2 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 7262advs-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | Data only until ~23 Nov. '03 due to biofouling |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USGS-WH | ABS #278-018 | 90 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7264abss-cal.nc | ---------------- | ---------------- | ---------------- |  |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USC | P #1417097 | 174.5 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7261advs-a.nc | ---------------- | ---------------- |  |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USC | P #1276950 | 183.5 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7262advs-a.nc | ---------------- | ---------------- |  |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USGS-WH | CT #265 | 225.5 cmab |  | 300s |  | large flow tripod | 7261sc-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USC | Rotating Sonar #1487 | 45 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USC | OBS #1551 | 27 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7261advs-a.nc | ---------------- | ---------------- | ---------------- |  |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | USC | OBS #1555 | 57 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7262advs-a.nc | ---------------- | ---------------- | ---------------- |  |
| 726 | Myrtle Beach | 6 | 33° 42.411′ N | 78° 45.617′ W | 10.6 m | 1 | 10/28/2003 | 1/22/2004 | GT | ADP #67 | 265.5 cmab |  | 900 s |  | large flow tripod | ---------------- | ---------------- | 7263arc-a.nc | 7263arwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | ADV #1 B277 | 48 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 7281advs-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | Data only until ~23 Nov. '03 due to biofouling |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | ADV #2 B268 | 48 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 7282adv-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | Data only until ~23 Nov. '03 due to biofouling |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | P #47037 | 165 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7281adv-a.nc | ---------------- | ---------------- |  |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | CT #3030 | 169 cmab |  | 3600 s |  | large flow tripod | 7282advs-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-MP | PCADP #H40 | 110 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 728pcvp-cal2.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | P #60005 | 163 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 728pcvp-cal2.nc | ---------------- | ---------------- |  |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | OBS #2181 | 60 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 728pcvp-cal2.nc | ---------------- | ---------------- | ---------------- |  |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | OBS #2182 | 120 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 728pcvp-cal2.nc | ---------------- | ---------------- | ---------------- |  |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | OBS #1244 | 30 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | adv7282vp-cal2.nc | ---------------- | ---------------- | ---------------- |  |
| 728 | Myrtle Beach | 7A | 33° 43.348′ N | 78° 46.747′ W | 10.6 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | OBS #2277 | 90 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | adv7282vp-cal2.nc | ---------------- | ---------------- | ---------------- |  |
| 729 | Myrtle Beach | 7A | 33° 43.364′ N | 78° 46.761′ W | 10.46 m | 1 | 10/4/2003 | 1/21/2004 | USGS-WH | CT #728 | 1mbs |  | 300 s |  | USGS surface buoy | 7291mc-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | CT #461 for 2nd half |
| 731 | Myrtle Beach | 8 | 33° 43.020′ N | 78° 46.290′ W | 9.4 m | 1 | 10/26/2003 | 1/29/2004 | USC | AquaDopp #445 | 48 cmab |  | 900 s |  | miniature tripod | ---------------- | ---------------- | 7311aqc-a.nc | 7311aqwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 732 | Myrtle Beach | 7B | 33° 43.340′ N | 78° 46.837′ W | 11.1 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | ADCP #2054 | 208 cmab |  | 900 s | 5 min every 15 min | small tripod | ---------------- | ---------------- | 7321adc-a.nc | 7321adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 732 | Myrtle Beach | 7B | 33° 43.340′ N | 78° 46.837′ W | 11.1 m | 1 | 10/28/2003 | 1/21/2004 | USGS-MP | ABS #278-017 | 89 cmab |  | 3600 s |  | small tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7322abss-cal.nc | ---------------- | ---------------- | ---------------- |  |
| 732 | Myrtle Beach | 7B | 33° 43.340′ N | 78° 46.837′ W | 11.1 m | 1 | 10/28/2003 | 1/21/2004 | USGS-WH | Imagenex Rot. Sonar #1751 | 55/104 cmab (Fan/Pencil) |  | 900 s | 5 min every 15 min | small tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7323Aim-cal.nc | 7323Bim-cal.nc |  |
| 733 | Myrtle Beach | 4 | 33° 42.050′ N | 78° 47.110′ W | 9.9 m | 1 | 10/28/2003 | 1/21/2004 | GT | ADCP #2913 | 44.5 cmab |  | 900 s | 5 min every 15 min | TRBM | ---------------- | ---------------- | 7331adc-a.nc | 7331adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 730 | Myrtle Beach | 5 | 33° 44.113′ N | 78° 45.414′ W | 9.6 m | 1 + 2 | 10/28/2003 | 4/23/2004 | USC | ADCP #832 | 58.5 cmab |  | 900 s | 5 min every 15 min | TRBM | ---------------- | ---------------- | No Data | No Data | ---------------- | ---------------- | ---------------- | ---------------- | Instrument was not recovered at the end of deployment 1 |
| 740 | Myrtle Beach | 1 | 33° 38.970′ N | 78° 47.404′ W | 11.6 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | ADCP #159 | 125 cmab |  | 900 s | 5 min every 15 min | micropod | ---------------- | ---------------- | 7401adc-a.nc | 7401adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 742 | Myrtle Beach | 2 | 33° 38.922′ N | 78° 50.941′ W | 9.2 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | ADCP #767 | 124 cmab |  | 900 s | 5 min every 15 min | micropod | ---------------- | ---------------- | 7421adc-a.nc | 7421adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 742 | Myrtle Beach | 2 | 33° 38.922′ N | 78° 50.941′ W | 9.2 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | CT #1045 | 101 cmab |  | 300 s |  | micropod | 7422sc-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 742 | Myrtle Beach | 2 | 33° 38.922′ N | 78° 50.941′ W | 9.2 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | PT #127 | 45 cmab |  | 300 s |  | micropod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7423pt-a.nc | ---------------- | ---------------- |  |
| 743 | Myrtle Beach | 2 | 33° 38.959′ N | 78° 50.959′ W | 9.3 m | 2 | 1/21/2004 | 4/24/2004 | USGS-WH | CT #307 | 1 mbs |  | 300 s |  | USGS surface buoy | 7431mc-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | MC #707 for 1st half |
| 744 | Myrtle Beach | 3 | 33° 46.470′ N | 78° 40.893′ W | 10.6 m | 2 | 1/29/2004 | 4/23/2004 | USC | ADCP #2014 | 125 cmab |  | 900 s | 5 min every 15 min | micropod | ---------------- | ---------------- | 7441adc-a.nc | 7441adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 744 | Myrtle Beach | 3 | 33° 46.470′ N | 78° 40.893′ W | 10.6 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | CT #392 | 99 cmab |  | 300 s |  | micropod | 7442sc-b.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | Data stops in Feb. 2004 |
| 744 | Myrtle Beach | 3 | 33° 46.470′ N | 78° 40.893′ W | 10.6 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | PT #128 | 45 cmab |  | 300 s |  | micropod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7443pt-a.nc | ---------------- | ---------------- |  |
| 745 | Myrtle Beach | 3 | 33° 46.470′ N | 78° 40.906′ W | 10.8 m | 2 | 1/21/2004 | 4/24/2004 | USGS-WH | CT #263 | 1mbs |  | 300 s |  | USGS surface buoy | 7451mc-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | MC #726 for 1st half. Data stops on 25-Mar-2004 |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | USC | ADV #A300 | 39.3 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 7461advs-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | USC | ADV #A302 | 50.2 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 7462advs-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | USC | P #1417097 | 174.5 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7461advs-a.nc | ---------------- | ---------------- |  |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | USC | P #1276950 | 183.5 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7462advs-a.nc | ---------------- | ---------------- |  |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | USC | OBS #1551 | 27 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7461advs-a.nc | ---------------- | ---------------- | ---------------- |  |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | USC | OBS #1555 | 57 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7462advs-a.nc | ---------------- | ---------------- | ---------------- |  |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | GT | ADP #67 | 265.5 cmab |  | 900 s | 5 min every 15 min | large flow tripod | ---------------- | ---------------- | 7463arc-a.nc | 7463arwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | USC | ABS #706-030 | 90 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7464abss-cal.nc | ---------------- | ---------------- | ---------------- | Data one day ahead b/c of laptop used to program it |
| 746 | Myrtle Beach | 6 | 33° 42.402′ N | 78° 45.640′ W | 9.0 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | CT #265 | 225.5 cmab |  | 300 s |  | large flow tripod | 7464Asc-a.nc | 7464Bsc-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-MP | ABS #278-018 | 103 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7484abss-cal.nc | ---------------- | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-MP | PCADP #H40 | 102 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 748pcvp-cal2.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | P #60005 | 172 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 748pcvp-cal2.nc | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | CT #2945 | 174 cmab |  | 3600 s |  | large flow tripod | 7482adv-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | OBS #2181 | 60 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 748pcvp-cal2.nc | ---------------- | ---------------- | ---------------- | OBS#2182 damaged during tripod assembly |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | ADV #B277 | 53 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 7481advs-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | ADV #B268 | 54 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | 7482advs-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | P #47037 | 169 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7481advs-a.nc | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | OBS #1244 | 30 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7482advs-a.nc | ---------------- | ---------------- | ---------------- |  |
| 748 | Myrtle Beach | 7A | 33° 43.331′ N | 78° 46.762′ W | 9.8 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | OBS #2277 | 90 cmab |  | 3600 s |  | large flow tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7482advs-a.nc | ---------------- | ---------------- | ---------------- |  |
| 749 | Myrtle Beach | 7A | 33° 46.364′ N | 78° 46.761′ W | 10.46 m | 2 | 1/21/2004 | 4/24/2004 | USGS-WH | CT #461 | 1 mbs |  | 300 s |  | USGS surface buoy | 7491mc-a.nc | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | CT #728 for 1st half |
| 751 | Myrtle Beach | 8 | 33° 43.027′ N | 78° 46.306′ W | 8.3 m | 2 | 1/30/2004 | 4/23/2004 | USC | AquaDopp #445 | 48 cmab |  | 900 s | 5 min every 15 min | miniature tripod | ---------------- | ---------------- | 7511aqc-a.nc | 7511aqwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 752 | Myrtle Beach | 7B | 33° 43.325′ N | 78° 46.823′ W | 9.6 m | 2 | 1/29/2004 | 4/23/2004 | USGS-MP | ABS #278-017 | 88.5 cmab |  | 3600 s | 22 min every 1 hr | small tripod | ---------------- | ---------------- | ---------------- | ---------------- | 7522abss-cal.nc | ---------------- | ---------------- | ---------------- |  |
| 752 | Myrtle Beach | 7B | 33° 43.325′ N | 78° 46.823′ W | 9.6 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | Imagenex Rot. Sonar Fan | 53 cmab |  | 5 hr | 1 cycle every 5 hr | small tripod | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | ---------------- | 7521Aim-cal.nc | 7521Bim-cal.nc |  |
| 752 | Myrtle Beach | 7B | 33° 43.325′ N | 78° 46.823′ W | 9.6 m | 2 | 1/29/2004 | 4/23/2004 | USGS-WH | ADCP #2054 | 206 cmab |  | 900 s | 5 min every 15 min | small tripod | ---------------- | ---------------- | 7521adc-a.nc | 7521adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |
| 753 | Myrtle Beach | 4 | 33° 42.040′ N | 78° 47.091′ W | 8.9 m | 2 | 1/29/2004 | 4/23/2004 | GT | ADCP #2913 | 44.5 cmab |  | 900 s | 5 min every 15 min | TRBM | ---------------- | ---------------- | 7531adc-a.nc | 7531adwp-cal.nc | ---------------- | ---------------- | ---------------- | ---------------- |  |