Day: 11/07/02

Latitude: 28°14.60 N

Water depth: 1027 m

Core number: MD02-2564 GHF

GMT time: 16:18

Longitude: 89°09.27 W

Location: Kane Spur

Corer type: Gravity /Flux core

Corer length: 17 m

Core length: 7.63 m

Observations

Corer condition: Heat flux measurements, several triggers: GHF1 28°14.60 N, 89°09.27 W, GHF2 28°13.34 N, 89°05.31 W, GHF3 28°12.31 N 89°01.2034 W, GHF4 28°12.32 N, 89°01.20 W

Core condition: Good. The bottom of the core is disturbed eventually by coring or gas hydrate melting.

Sections and Sampling

Number of sections recovered and conditions:

6 sections of 1.5m were recovered; the last section measures 13 cm

Onboard sampling and post cruise processing:

- Both the working and archive halves will be stored at Texas A&M University

- Two bags were recovered: 1 core catcher, 1 core top.

- USGS core measurements and activities : Thermal conductivity ( Univ.Victoria)

- MST magnetic susceptibility, gamma ray attenuation and p-wave measurements were made downcore, at a resolution of 2 cm. Colour measurements were taken every 2 cm.

## Summary of physical and sedimentological observations

Dominant lithologies: 0-207 cm, light greenish gray slightly bioturbated silty clay with abundant foraminifers and nannofossils. 207-750 cm, dark greenish to greenish black silty clay with some laminations. 216-281 cm, heavily bioturbated interval.

Minor lithologies: None