Seismic Operations During Cruise IMAGES VIII, MONA/PAGE 2002, D-1-02-GM Cruise of the R/V Marion Dufresne in the Northern Gulf of Mexico

Patrick E. Hart and Thomas D. Lorenson

High-resolution chirp seismic refection profiles were collected at most of the 2002 core sites using a hull-mounted Thales Sea Falcon II chirp seismic system, using a 25 ms chirp source with a 1600 Hz bandwidth centered at 3.75 kHz.  The system was operating almost continuously during the cruise, recording approximately 600 files in standard geophysical 16-bit SEG-Y format, which were later concatenated into 12 larger files.  The 40 SEG-Y files available on the USGS website, http://walrus.wr.usgs.gov/infobank/d/d102gm/html/d-1-02-gm.meta.html were taken from these 12 files and comprise the tracklines designed to pass through and adjacent to the coring sites.   The final SEG-Y data files each contain a SEG-Y EBCDIC file header (shown below) listing important information about the data and the data trace headers.  The most important trace header information is longitude and latitude, given as 4 byte integers in trace header locations bytes 191-194 and 195-198, respectively.  The values are decimal degrees, with five decimal places, multiplied by 100,000 to allow the values to remain integer.  For example, a latitude of 27.29863 degrees will be recorded in the trace header as 2729863.

Table 1.  SEG-Y EBCDIC header.

**********************

* EBCDIC REEL HEADER *

**********************

C 1 U. S.  GEOLOGICAL SURVEY                     COASTAL AND MARINE GEOLOGY TEAM

C 2 SURVEY_ID:  D1-02-GM                         YEAR:  2002

C 3 AREA:   NORTHERN GULF OF MEXICO              VESSEL: R/V MARION DUFRESNE

C 4

C 5 INSTRUMENT: THALES UNDERWATER SYSTEMS SEAFALCON II CHIRP SEISMIC

C 6             25 MS CHIRP LENGTH   1600 HZ BANDWIDTH CENTERED AT 3.75KHZ

C 7             LINEAR FREQUENCY MODULATED CHIRP

C 8 RECORDING PARAMETERS:                        CHANNELS PER SHOT:  1

C 9        SAMPLE INTERVAL: 417  MICROSEC        SAMPLE FREQUENCY:  2.4KHZ

C10        SAMPLES/TRACE: 2048                 DATA LENGTH:  850 MSEC

C11         RECORD LENGTH VARIES WITH DEEP WATER DELAY PLUS DATA LENGTH

C12              DATA TRACE IS AMPLITUDE ENVELOPE; POSITIVE VALUES ONLY

C13

C14

C15 RECORDING FORMAT:

C16        SEG-Y 16-BIT INTEGER

C17 IMPORTANT TRACE HEADER VALUE LOCATIONS:

C18    NAME    BYTES       TYPE       DESCRIPTION

C19   FFID       9-12    INTEGER      FIELD FILE, SHOT OR PING NUMBER

C20   CDP        21-24   INTEGER      SAME AS FFID

C21

C22   TYPE      29-30    INTEGER      TRACE IDENTIFFICATION CODE

C23

C24

C25   DELAY    109-110   INTEGER      DELAY RECORDING TIME IN MILLISEC

C26   NSAMPLES 115-116   INTEGER      NUMBER OF SAMPLES IN THIS TRACE

C27   SRATE    117-118   INTEGER      SAMPLE INTERVAL IN MICROSEC FOR THIS TRACE

C28   YEAR     157-158   INTEGER      YEAR DATA RECORDED

C29   DAY      159-160   INTEGER      DAY OF YEAR

C30   HOUR     161-162   INTEGER      HOUR (24-HOUR CLOCK)

C31   MINUTE   163-164   INTEGER      MINUTE

C32   SECOND   165-166   INTEGER      SECOND

C33   LONGITUDE 191-194  INTEGER      DECIMAL DEGREES TIMES 100000

C34   LATITUDE  195-198  INTEGER      DECIMAL DEGREES TIMES 100000

C35

C36   FOR FURTHER INFORMATION CONCERNING THIS DATASET, CONTACT:

C37     PATRICK HART

C38     U. S. GEOLOGICAL SURVEY, M/S 999

C39     345 MIDDLEFIELD RD., MENLO PARK, CALIFORNIA  94025

C40     (650) 329-5160    INTERNET:  HART@USGS.GOV

The SEG-Y data traces are the calculated amplitude envelope attribute showing positive values only, as opposed to a conventional wiggle trace with positive and negative values.  The firing or chirp interval during data acquisition was 1.3 seconds for lines SP1b, SP2 and SP3 and 4.3 seconds for lines SP15 and SP16.  For all other lines this interval was 3.5 seconds.  Sample interval of the data is 417 microseconds with 2048 samples per trace, giving a data length of 850 milliseconds.  The data were recorded with a variable deep-water delay calculated in real-time based on the water depth.  In theory, this will give a constant record length below seafloor, but in practice the bottom-tracking feature occasionally loses the bottom and this causes skipped or blank traces in the final display.  This is evident on some of the Tiff image files of the seismic lines, such as line SP15 or SP33a.  The SEG-Y files are output with the deep-water delay applied.

In addition to the SEG-Y format files, a Tiff image file of each seismic line is available on the USGS website http://walrus.wr.usgs.gov/infobank/d/d102gm/html/d-1-02-gm.meta.html.  These are grayscale Tiff format files with LZW compression.  The display parameters of the data in these Tiff files are 15 inches/second and either 40 or 100 traces/inch.  The horizontal scale is dependent on the chirp interval, ship speed and the traces/inch of the plot.  To accurately determine horizontal distance along one of these seismic profiles, refer to the navigation file (D102GM_lines.xls) available on the USGS website http://walrus.wr.usgs.gov/infobank/d/d102gm/html/d-1-02-gm.meta.html.  This spreadsheet lists position in decimal degrees versus time in GMT at 7 to 12 second intervals along each profile.  A good estimate of horizontal scale for each line can be determined from the line summary table below, which lists line length and plotting parameters.

GMT is listed along the top of each seismic profile as hhmmss  (hour,minute,second).  Time is also in the standard SEG-Y trace header locations as described in the EBCDIC header.   All of the profiles are plotted with north and west on the left.  Two-way reflection time in 10 ms intervals is listed along the sides of the seismic profiles in the Tiff images.  Using a seismic velocity of 1500 m/s, each 10 ms represents approximately 7.5 meters of sediment.  A reduced image of line SP17, a west-to-east profile crossing Bush Hill, is shown below in Figure 2a.

Fig. 2a.  This image of seismic line SP17 was modified from the tiff image SP17.tif available on the USGS website http://walrus.wr.usgs.gov/infobank/d/d102gm/html/d-1-02-gm.meta.html.  The size was reduced to fit on the page, and the title, scale bars, and the locations of cores MD02-2564, 2565, and 2566 were added.  The data show good signal-to-noise ratio and approximately 100 to 150 m penetration into the soft sediments adjacent to the mound at the left-center of the figure.  There is very little imaging beneath the hard carbonate and gas hydrate that occurs at the surface of this and similar mounds in the region.  The location of this profile is shown on the Bush Hill map in Fig 4.  At this reduced scale the GMT and two-way reflection time labels are not visible.  The boxed area is expanded below in Figure 2b.

Figure 2b.  This expanded view of a portion of line SP17 allows the GMT and reflection time labels to be read.   Two-way reflection time from 600 ms to 840 ms in 10 ms intervals is labeled along the left and GMT from hour 16, minute 55, second 08 to hour 17, minute 00, second 56 is labeled along the top from right to left.  The 35 second GMT label interval represents 10 traces at a 3.5 second chirp interval. This labeling is on all the Tiff image files.

Collecting geophysical data was not the highest cruise priority so the seismic coverage at each core site depends on the time available between coring operations.  Trackline maps for the six areas where seismic data were acquired are shown in figures 3 through 8.  The initial series of seismic lines at Tunica mound were poorly navigated and many lines were run in a fairly small area.  As a result the lines are not straight and cross back and forth over each other.  Figure 3a shows all the Tunica lines and figures 9b and 9c each plot a subset of the lines in order to be more legible.  An additional problem with the Tunica lines is that the primary navigation recording system was not operating during the acquisition of lines SP1 to SP3, and lines SP6 through SP10.  The navigation fixes for these lines were taken from the SEG-Y trace headers as described above.  The precision of the fixes (approximately 10 m) in the trace headers is not as high as with the primary system (approximately 1 m) and therefore these lines appear to be choppier than the others when plotted at a large scale.

A table of information on all the chirp seismic lines is listed below and included on this CD in file “line_summary.xls”.  Three of the recovered cores do not have corresponding chirp seismic lines that pass near their locations.  For these cores, MD02-2566, 2567 and 2567, files were made of the chirp data recorded while the ship was drifting during coring operations.  These are listed as lines 24d, 25d, and 33d.

Table 2. Chirp seismic reflection line summary

| Line | Area | Length | JD | Start time | End time | Number | Tiff Scale | Line scale | Ave speed |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| no. |  | km |  | hour-min | hour-min | traces | inch/km | traces/km | kts |
| 1a | Tunica Mound | 2.6 | 185 | 1812 | 1818 | 106 | 1.0 | 40.8 | 14.0 |
| 1b | Tunica Mound | 7.3 | 185 | 1818 | 1838 | 916 | 1.3 | 125.5 | 11.8 |
| 2 | Tunica Mound | 10.7 | 185 | 1841 | 1921 | 1850 | 1.7 | 172.9 | 8.7 |
| 3 | Tunica Mound | 4.6 | 185 | 1937 | 1956 | 856 | 1.9 | 186.1 | 7.8 |
| 4 | Tunica Mound | 2.8 | 186 | 403 | 422 | 861 | 3.1 | 307.5 | 4.8 |
| 5 | Tunica Mound | 3.6 | 186 | 433 | 500 | 1227 | 3.4 | 340.8 | 4.3 |
| 6 | Tunica Mound | 4.1 | 187 | 910 | 938 | 483 | 2.9 | 117.8 | 4.7 |
| 7 | Tunica Mound | 3.0 | 187 | 941 | 959 | 311 | 2.6 | 103.7 | 5.4 |
| 8 | Tunica Mound | 2.5 | 187 | 1228 | 1246 | 309 | 3.1 | 123.6 | 4.5 |
| 9 | Tunica Mound | 2.1 | 187 | 1252 | 1304 | 207 | 2.5 | 98.6 | 5.7 |
| 10 | Tunica Mound | 2.2 | 187 | 1312 | 1328 | 274 | 3.1 | 124.5 | 4.5 |
| 11 | Tunica Mound | 2.2 | 187 | 1344 | 1358 | 241 | 2.7 | 109.5 | 5.1 |
| 12 | Tunica Mound | 1.0 | 187 | 1423 | 1431 | 138 | 3.5 | 138.0 | 4.0 |
| 13 | Tunica Mound | 1.2 | 187 | 1439 | 1446 | 121 | 2.5 | 100.8 | 5.6 |
| 14 | Tunica Mound | 2.1 | 187 | 1653 | 1731 | 656 | 7.8 | 312.4 | 1.8 |
| 15 | Pigmy Basin | 6.7 | 190 | 537 | 620 | 603 | 2.3 | 90.0 | 5.0 |
| 16 | Pigmy Basin | 5.4 | 190 | 644 | 716 | 449 | 2.1 | 83.1 | 5.5 |
| 17 | Bush Hill | 6.0 | 190 | 1625 | 1701 | 610 | 2.5 | 101.7 | 5.4 |
| 18 | Bush Hill | 3.0 | 190 | 1722 | 1739 | 293 | 2.4 | 97.7 | 5.7 |
| 19 | Bush Hill | 2.8 | 190 | 1746 | 1802 | 276 | 2.5 | 98.6 | 5.7 |
| 20 | Bush Hill | 2.2 | 190 | 1813 | 1828 | 259 | 2.9 | 117.7 | 4.8 |
| 21a | Kane Spur | 21.0 | 192 | 444 | 646 | 2001 | 1.0 | 95.3 | 5.9 |
| 21b | Kane Spur | 19.3 | 192 | 935 | 1120 | 1811 | 0.9 | 93.8 | 6.0 |
| 22a | Kane Spur | 9.6 | 192 | 1224 | 1326 | 1070 | 1.1 | 111.5 | 5.0 |
| 22b | Kane Spur | 26.4 | 192 | 1650 | 1919 | 2569 | 1.0 | 97.3 | 5.7 |
| 23a | Kane Spur | 31.1 | 193 | 35 | 308 | 2639 | 0.8 | 84.9 | 6.6 |
| 23b | Kane Spur | 5.5 | 193 | 530 | 604 | 580 | 1.1 | 105.5 | 5.2 |
| 24 | Kane Spur | 27.4 | 193 | 649 | 908 | 2398 | 0.9 | 87.5 | 6.4 |
| 24d | Kane Spur | drift | 194 | 900 | 930 | 517 | drift | drift | drift |
| 25 | Kane Spur | 23.0 | 194 | 342 | 542 | 2067 | 0.9 | 89.9 | 6.2 |
| 25d | Kane Spur | drift | 194 | 1457 | 1527 | 485 | drift | drift | drift |
| 26 | West MC | 10.8 | 195 | 622 | 722 | 1035 | 1.0 | 95.8 | 5.8 |
| 27 | West MC | 4.8 | 195 | 1220 | 1252 | 552 | 1.2 | 115.0 | 4.9 |
| 28 | West MC | 6.0 | 195 | 1303 | 1340 | 638 | 1.1 | 106.3 | 5.3 |
| 29 | West MC | 10.7 | 195 | 1925 | 2023 | 1000 | 0.9 | 93.5 | 6.0 |
| 30 | West MC | 11.1 | 195 | 2035 | 2143 | 1172 | 1.1 | 105.6 | 5.3 |
| 31 | West MC | 6.6 | 195 | 2149 | 2225 | 621 | 0.9 | 94.1 | 5.9 |
| 32 | Central MC | 6.4 | 195 | 219 | 242 | 396 | 0.6 | 61.9 | 9.0 |
| 32d | Central MC | drift | 195 | 335 | 405 | 517 | drift | drift | drift |
| 33a | Central MC | 9.5 | 196 | 37 | 105 | 483 | 0.5 | 50.8 | 11.0 |
| 33b | Central MC | 0.9 | 196 | 212 | 250 | 655 | 7.3 | 727.8 | 0.8 |

The two tables below are a summary of all the Marion Dufresne cores and are combined in the spreadsheet file on this CD  “core_seismic.xls”.  The one or two chirp seismic lines that pass over or near each core are listed with the core location along the line in time (GMT).

Table 3.  Seismic reflection line ties with core locations.

| CORE ID | Latitude | Longitude | Chirp Seismic Tie 1 | Chirp Seismic Tie 2 |
| --- | --- | --- | --- | --- |
|  |  |  | distance from line to core | distance from line to core |
| MD02-2535 | 27.61983 | -92.24100 | SP2; 185 190955; 10 m N | SP11; 187 135555; on line |
| MD02-2536GHF-1 | 27.62268 | -92.24378 | SP12;187 142955; on line | SP8; 187 123210; 20 m NW |
| MD02-2536GHF-2 | 27.62530 | -92.24600 | SP12; 187 143100; 220 m NW | none |
| MD02-2536GHF-3 | 27.62700 | -92.23750 | SP7; 187 95640; 170 m N | none |
|  | 27.61600 | -92.24867 | SP1a; 185 181435; on line | SP2; 185 191310; 30 m NW |
| MD02-2538G | 27.61667 | -92.24717 | SP1a; 185 181500; 20 m N | SP2; 185 191235; 30 m N |
| MD02-2539 | 27.63983 | -92.19226 | SP2; 185 184940; 80 m N | none |
| MD02-2540GHF-1 | 27.64008 | -92.19201 | SP2; 185 184935; 100 m N | none |
| MD02-2540GHF-2 | 27.64017 | -92.19533 | SP2; 185 185050; 190 m N | none |
| MD02-2541 | 27.63244 | -92.21245 | SP2; 185 185750; 160 m NW | none |
| MD02-2542GHF | 27.63212 | -92.21242 | SP2; 185 185750; 140 m NW | none |
| MD02-2543G | 27.61253 | -92.25565 | SP1a; 185 181250; 50 m SE | none |
| MD02-2544G | 27.61315 | -92.25336 | SP10; 187 132425; 20 m N | SP2; 185 191520; 30 m N |
| MD02-2545G | 27.61416 | -92.25177 | SP10 187 132255; on line | SP2; 185 191435; 20 m NW |
| MD02-2546 | 27.61567 | -92.24697 | SP11; 187 135125; 30 m SE | SP2; 185 191245; 80 m SE |
| MD02-2547GHF | 27.61642 | -92.24832 | SP1a; 185 181445; 30 m NW | SP2; 185 191300; 60 m NW |
| MD02-2553C2 | 27.18340 | -91.41694 | SP15; 190 55650; on line | SP16; 190 65950; 40 m N |
| MD02-2554 | 27.78371 | -91.49967 | SP17; 190 164820; on line | SP18; 190 172810; 50 m E |
| MD02-2555 | 27.78320 | -91.48901 | SP17; 190 164210; 50 m S | SP19; 190 175540; on line |
| MD02-2556 | 27.78300 | -91.47809 | SP17; 190 163520;90 m S | SP20; 190 182010; 30 m W |
| MD02-2557GHF1 | 27.78304 | -91.49862 | SP17; 190 164740; 70 m S | SP18; 190 172830; 150 m E |
| MD02-2557GHF2 | 27.78310 | -91.48904 | SP17; 190 164210; 50 m S | SP19; 190 175540; on line |
| MD02-2557GHF3 | 27.78288 | -91.47720 | SP17; 190 163445; 100 m S | SP20; 190 182015; 50 m E |
| MD02-2559 | 28.22267 | -89.08784 | SP21a; 192 62815; on line | SP25; 194 53730; 60 m SE |
| MD02-2560 | 28.24361 | -89.15503 | SP21a; 192 54910; 40 m N | none |
| MD02-2561 | 28.20530 | -89.02016 | SP21b; 192 100640; 20 m N | SP23a; 193 13540; 20 m NW |
| MD02-2562 | 28.07997 | -89.14030 | SP23a; 193 30800; 170 m SW | none |
| MD02-2563C2 | 28.12354 | -89.13651 | SP24; 193 72140; 230 m N | none |
| MD02-2564GHFa | 28.24347 | -89.15464 | SP21a; 192 54925; 40 m N | none |
| MD02-2564GHFb | 28.22257 | -89.08861 | SP25; 194 53710; 10 m SE | SP21a; 192 62755; 50 m SW |
| MD02-2564GHFc | 28.20545 | -89.02014 | SP21b; 192 100640; 30 m N | SP23a; 193 13535; 30 m NW |
| MD02-2564GHFd | 28.20733 | -89.02019 | SP23a; 193 13450; 170 m NW | none |
| MD02-2565 | 28.12361 | -89.13971 | SP24; 193 72000; 130 m N | none |
| MD02-2566 | 28.11927 | -89.10339 | SP23a; 193 235 30; 660 m NW | SP24d; 194 91630; on line |
| MD02-2567 | 28.10037 | -89.02007 | SP24; 193 82700; 1750 m NE | SP25d; 194 151730; on line |
| MD02-2568GHFa | 28.07992 | -89.14030 | SP23a; 193 30800; 170 m SW | none |
| MD02-2568GHFb | 28.08107 | -89.13717 | SP23a; 193 30610; 100 m SE | none |
| MD02-2568GHFc | 28.11936 | -89.10331 | SP23a; 193 235 30; 660 m NW | SP24d; 194 92850; on line |
| MD02-2568GHFd | 28.12347 | -89.13952 | SP24; 193 72010; 120 m N | none |
| MD02-2568GHFe | 28.12354 | -89.13636 | SP24; 193 72150; 240 m N | none |
| MD02-2569 | 28.15218 | -89.47980 | SP33b; 196 21200; 20 m SW | SP32d; 195 33800; on line |
| MD02-2570 | 28.07107 | -89.68997 | SP26; 195 65720; 20 m S | SP31; 195 222450; 60 m NW |
| MD02-2571C2 | 28.06681 | -89.72007 | SP26; 195 64020; 90 m S | SP28; 195 132315; 150 m W |
| MD02-2572GHF | 28.07109 | -89.69001 | SP26; 195 65720; 20 m S | SP31; 195 222450; 60 m NW |
| MD02-2573GHF | 28.15204 | -89.48004 | SP33b; 196 21200; 50 m SW | SP32d; 195 34200; on line |

Table 4.  Recovered core summary

| CORE ID | Latitude | Longitude | Site Name | Core Length | Water Depth |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | meters | meters |
| MD02-2535 | 27.61983 | -92.24100 | Tunica Mound | 37.84 | 605 |
| MD02-2536GHF-1 | 27.62268 | -92.24378 | Tunica Mound | 8.88 | 608 |
| MD02-2536GHF-2 | 27.62530 | -92.24600 | Tunica Mound | none | 564 |
| MD02-2536GHF-3 | 27.62700 | -92.23750 | Tunica Mound | none | 585 |
|  | 27.61600 | -92.24867 | Tunica Mound | 33.58 | 600 |
| MD02-2538G | 27.61667 | -92.24717 | Tunica Mound | 7.76 | 599 |
| MD02-2539 | 27.63983 | -92.19226 | Tunica Mound | 31.10 | 622 |
| MD02-2540GHF-1 | 27.64008 | -92.19201 | Tunica Mound | 5.65 | 617 |
| MD02-2540GHF-2 | 27.64017 | -92.19533 | Tunica Mound | none | 620 |
| MD02-2541 | 27.63244 | -92.21245 | Tunica Mound | 35.34 | 615 |
| MD02-2542GHF | 27.63212 | -92.21242 | Tunica Mound | 7.70 | 617 |
| MD02-2543G | 27.61253 | -92.25565 | Tunica Mound | 0.15 | 579 |
| MD02-2544G | 27.61315 | -92.25336 | Tunica Mound | 0.10 | 584 |
| MD02-2545G | 27.61416 | -92.25177 | Tunica Mound | 9.27 | 588 |
| MD02-2546 | 27.61567 | -92.24697 | Tunica Mound | 31.21 | 595 |
| MD02-2547GHF | 27.61642 | -92.24832 | Tunica Mound | 5.73 | 607 |
| MD02-2553C2 | 27.18340 | -91.41694 | Pigmy Basin | 10.32 | 2259 |
| MD02-2554 | 27.78371 | -91.49967 | Bush Hill | 31.05 | 602 |
| MD02-2555 | 27.78320 | -91.48901 | Bush Hill | 35.68 | 636 |
| MD02-2556 | 27.78300 | -91.47809 | Bush Hill | 34.25 | 654 |
| MD02-2557GHF1 | 27.78304 | -91.49862 | Bush Hill | 5.59 | 613 |
| MD02-2557GHF2 | 27.78310 | -91.48904 | Bush Hill | none | 639 |
| MD02-2557GHF3 | 27.78288 | -91.47720 | Bush Hill | none | 659 |
| MD02-2559 | 28.22267 | -89.08784 | Kane Spur | 33.39 | 1132 |
| MD02-2560 | 28.24361 | -89.15503 | Kane Spur | 28.24 | 1029 |
| MD02-2561 | 28.20530 | -89.02016 | Kane Spur | 28.80 | 1268 |
| MD02-2562 | 28.07997 | -89.14030 | Kane Spur | 26.09 | 1051 |
| MD02-2563C2 | 28.12354 | -89.13651 | Kane Spur | 3.86 | 1070 |
| MD02-2564GHFa | 28.24347 | -89.15464 | Kane Spur | 7.63 | 1027 |
| MD02-2564GHFb | 28.22257 | -89.08861 | Kane Spur | none | 1261 |
| MD02-2564GHFc | 28.20545 | -89.02014 | Kane Spur | none | 1269 |
| MD02-2564GHFd | 28.20733 | -89.02019 | Kane Spur | none | 1269 |
| MD02-2565 | 28.12361 | -89.13971 | Kane Spur | 22.50 | 1068 |
| MD02-2566 | 28.11927 | -89.10339 | Kane Spur | 26.05 | 1186 |
| MD02-2567 | 28.10037 | -89.02007 | Kane Spur | 26.65 | 1318 |
| MD02-2568GHFa | 28.07992 | -89.14030 | Kane Spur | 6.96 | 1049 |
| MD02-2568GHFb | 28.08107 | -89.13717 | Kane Spur | none | 1057 |
| MD02-2568GHFc | 28.11936 | -89.10331 | Kane Spur | none | 1190 |
| MD02-2568GHFd | 28.12347 | -89.13952 | Kane Spur | none | 1068 |
| MD02-2568GHFe | 28.12354 | -89.13636 | Kane Spur | none | 1049 |
| MD02-2569 | 28.15218 | -89.47980 | Central Miss | 10.35 | 1032 |
| MD02-2570 | 28.07107 | -89.68997 | West MC | 28.35 | 631 |
| MD02-2571C2 | 28.06681 | -89.72007 | West MC | 10.38 | 664 |
| MD02-2572GHF | 28.07109 | -89.69001 | West MC | 4.90 | 628 |
| MD02-2573GHF | 28.15204 | -89.48004 | Central MC | 4.20 | 1027 |

Figure 3a.   Trackline map for seismic profiles at the Tunica Mound core sites.  Core IDs are shown in this figure but line numbers are not, because the line spacing is too close to legibly show all line numbers in one page-size figure.  Figures 3b and 3c show lines 1 through 7, and 8 through 14, respectively.  Depth contours are in meters for this and all following maps.

Figure 3b.  Trackline map for seismic profiles 1 through 7 at the Tunica Mound core sites.

Figure 3c.  Trackline map for seismic profiles 8 through 14 at the Tunica Mound core sites.

Figure 4.  Trackline map for seismic profiles at the Pigmy Basin core site.

Figure 5.  Trackline map for seismic profiles at the Bush Hill core sites.

Figure 6.  Trackline map for seismic profiles at the Kane Spur core sites in the eastern Mississipi Canyon.

Figure 7.  Trackline map for seismic profiles at the West Mississippi core sites.

Figure 8.  Trackline map for seismic profiles at the Central Mississippi core sites.