Day: 11/07/02

Latitude: 28°12.31 N

Water depth: 1268 m

Core number: MD02-2561

GMT time: 22:26

Longitude: 89°01.21 W

Location: Kane Spur

Corer type: Calypso core

Corer length: 35.95 m

Core length: 28.8 m

Observations

Corer condition: Good

Core condition: Good. From 2000 cm to the end of the core, it is slightly then heavily disturbed.

Sections and Sampling

Number of sections recovered and conditions:

20 sections of 1.5m were recovered; the last section measures 30 cm

A 10 cm section was taken on each section, and one more on sections II, V, VIII, IX, XV, XIX,

Onboard sampling and post cruise processing:

- Both the working and archive halves will be stored at Texas A&M University

- the 10 cm sections were taken for pore water analysis (microbiology, and SO4-, Cl-, CH4, 14C, DIC)

- 1 bag of core top sediment was taken

- MST magnetic susceptibility, gamma ray attenuation and p-wave measurements were made downcore, at a resolution of 2 cm. Colour measurements were taken every 2 cm.

- USGS core measurements and activities : Elec. Resist ; Vane Shear , water content,  whole rounds for consol/triaxial (USGS-WH), Headspace Gas (USGS-Menlo Park), Thermal conductivity ( Univ.Victoria)

## Summary of physical and sedimentological observations

Dominant lithologies: 0-450 cm, light to dark greenish gray silty clay with moderate bioturbation and some foraminifers with decreasing content downcore. 450-900 cm dark greenish gray laminated silty clay. No foraminifer visible. 900-2880 clay on cm then silty clay, slightly bioturbated

Minor lithologies: Numerous silt layers at the bottom of the core, the first one being at 1430 cm.